## Slide 1
+1 (310) 876-8040 (US)
+31 (40) 209-1001 (EMEA)
info@ayyeka.com
www.ayyeka.com
Pinout: Serial Cable Assembly
Connect to Wavelet
M12 8-pin male
June 23, 2020
For technical support, contact:
support@ayyeka.com
+1 (310) 876-8040 Ext. 3 (US)
+31 (40) 209-1001 Ext. 3 (EMEA)
Panel connector #2
M12 8-pin male
Model WA00140

## Slide 2
+1 (310) 876-8040 (US)
+31 (40) 209-1001 (EMEA)
info@ayyeka.com
www.ayyeka.com
Pinout: Serial Cable Assembly for Wavelet V2 and Wavelet
WA1111-xx-V2 and WA1111-xx |  |  |  | 
Connector Pin # | Color | Signal | Pin Assignment | 
1 | White | RS232 TX | Front | Back
2 | Brown | Wavelet 12V Power Supply #4 (+) |  | 
3 | Green | Wavelet 12V Power Supply #3 (+) |  | 
4 | Yellow | SDI-12 |  | 
5 | Black | RS485 B |  | 
6 | Orange | RS485 A |  | 
7 | Blue | RS232 RX |  | 
8 | Red | Negative (-) |  | 
8
2
1
7
6
5
4
3
8
Note: xx represents the different models for US, EU, and SA
Model WA00140